Fri Jan 23 21:51:01 CST 2015
PROBLEM:
I have a "dirty" switch: it bounces a lot when pressed. The bounces can occur very quickly, on the order of only microseconds apart. The pin change interrupts on the ATmega chips act only on change of signal, and they trigger when any pin on a port (== up to 8 pins) is triggered. If you want to determine which pin actually triggered, that would take software and that means a delay from the moment of signal change to determining With a pin change interrupt enabled to trigger on the pin's port, how will the library react properly when this switch is pressed?

Notice that for Pin Change Interrupts, the interrupt can take place when any pin on the port is
interrupted. If you have the luxury of knowing ahead of time which pin(s) are interrupting, you
can design fast, custom code that will react to your simple situation. But remember that I am
writing a library: I don't know which pin may be doing the interrupting. So I have to survey the
pins to figure out which one(s) changed, and had triggered the interrupt. Furthermore, there is
an appreciable amount of time that it takes from the moment the triggering event happened to
when I enter the interrupt subroutine (ISR) and have gone through the logic to figure out which
pins did the triggering. ...How much time? That I aim to find out.

Why is this a big deal? Remember my bouncy switch? ...The interrupt triggers, the ISR starts up,
and the first thing I need to do is query the port to see the state of its pins. Well, some time
has elapsed since the triggering event and this query. In the course of that time, it's entirely
possible- and I'm writing this because it's not only possible, but it can happen quite readily-
that the state of the pin changes before I get a chance to sample it. So I get an interrupt but
it looks like a false alarm! The ISR never calls the user's function because none of the user's
interrupt pins appear to have changed.

There is no complete solution to this problem, because of the nature of Pin Change Interrupts.
All you can do is mitigate the situation. I will attempt to do so by capturing the state of the
port as early as possible in the ISR. The question is, how early is that?

I attempt a test:

The switch is connected as follows: A pin is configured as an input port, and the pullup resistor is on. Pin Change Interrupt is enabled on the pin (which will trigger on any level change). So when I press the switch, the signal goes from high to low and the interrupt is triggered. When I release, the signal goes from low to high and again there is an interrupt.

My ISR looks (in part) like this; this will turn on and off the Arduino Uno's pin 13 LED:

ISR(PORTC_VECT, ISR_NAKED) {
  uint8_t interruptMask;
  uint8_t ledon, ledoff;

  ledon=0b00100000; ledoff=0b0;

  PORTB=ledoff; // LOW
  PORTB=ledon; // HIGH
  PORTB=ledoff; // LOW
  PORTB=ledon; // HIGH
  PORTB=ledoff; // LOW
  (...)
}

The generated assembly code looks like this:
00000292 <__vector_4>:
  ledon=0b00100000; ledoff=0b0;

  PORTB=ledoff; // LOW
     292: 15 b8 out 0x05, r1 ; 5
  PORTB=ledon; // HIGH
     294: 80 e2 ldi r24, 0x20 ; 32
     296: 85 b9 out 0x05, r24 ; 5
  PORTB=ledoff; // LOW
     298: 15 b8 out 0x05, r1 ; 5
  PORTB=ledon; // HIGH
     29a: 85 b9 out 0x05, r24 ; 5
  PORTB=ledoff; // LOW
     29c: 15 b8 out 0x05, r1 ; 5

Notice a little optimization here: r1 is defined to always contain 0, so we don't even have to load
a value from memory (0 is an important number!). This makes the initial command very quick, and by using an oscilloscope we can see just how quickly the chip reacts after receiving the signal:

Look at the two vertical lines in the above screenshot- those are the cursors. ...So we are measuring 700 nanoseconds from when my switch first closed its connection (yellow trace) to where pin 13 went LOW (blue line). The cursor lines on the left and center-right tell the tale.

How much of that 700 nanoseconds was taken up by the first command itself, the one that signals us? That is:

292: 15 b8 out 0x05, r1 ; 5

In the blue trace, you can see that after I go low I go high, then low, then high again. The second dip- the shorter dip- above, should tell the tale. And it says:

(note that here I have zoomed in for a closer, more accurate look)

...Lo and behold, the trough- the PORTB=ledoff; is 62.4ns wide, which is equivalent to a 16.0MHz frequency, which is a single clock cycle of the ATmega328p. Note that the data sheet states that the OUT assembly instruction takes 1 cycle; the stars align!
Now- going back to the first picture: How long did it take to enter the ISR? My experiment measures the time from the switch close to the Pin13 going LOW. We can subtract the time to execute that command, and get to exactly how long it takes us to enter the ISR:

...That's 692ns measured, or approximately 11 cycles. Minus the 1 cycle that it took our command to run, it takes 10 cycles' time from interrupt to entering the ISR.
Thus, the best response to an interrupt that we could ever hope for is 630ns, more or less. That's at least 630 ns between activation and having a ghost of a chance to query the pins and store their value.
BUT! Can we just stuff an “in” command at the beginning of the ISR, in order to grab the port's pins' values? Not quite. An interrupt is by definition asynchronous- the computer never knows when it's going to happen. And the compiler writers are not able to know the myriad types of subroutines that will be necessary inside an interrupt. Thus they can never know which registers may be necessary for a user's ISR, and the implications of that are pretty significant. It means that the first thing the ISR should do is save the values of each and every register of the CPU. ...But isn't that expensive, time-wise? Why yes, yes it is. How so? Here is what the assembly looks like when I don't use NAKED_ISR; note the proper preamble to the ISR (there are reasons registers r2-r17 are not saved; suffice it to say they are scratch and their values are not guaranteed):
ISR(PORTC_VECT) {
     292: 1f 92 push r1
     294: 0f 92 push r0
     296: 0f b6 in r0, 0x3f ; 63
     298: 0f 92 push r0
     29a: 11 24 eor r1, r1
     29c: 2f 93 push r18
     29e: 3f 93 push r19
     2a0: 4f 93 push r20
     2a2: 5f 93 push r21
     2a4: 6f 93 push r22
     2a6: 7f 93 push r23
     2a8: 8f 93 push r24
     2aa: 9f 93 push r25
     2ac: af 93 push r26
     2ae: bf 93 push r27
     2b0: cf 93 push r28
     2b2: df 93 push r29
     2b4: ef 93 push r30
     2b6: ff 93 push r31
  uint8_t ledon, ledoff;

  ledon=0b00100000; ledoff=0b0;

  PORTB=ledoff; // LOW
     2b8: 15 b8 out 0x05, r1 ; 5

Now let's measure the time from interrupt to shutting off the Pin 13 LED again, just like before. It's given here:

...yikes! 3.12 microseconds! That's 50 times as long as 62.5 nanoseconds... which means, 50 machine cycles! Well, we do have 17 “push” instructions alone- at 2 cycles each, that's 32 * 62.5 right there.
This means it would be 3.12 microseconds- at least- from a triggering event, to querying the pins of the PORT, to see which pin triggered. That's painful. Is there anything we can do?
There is something: by hand-coding the preamble and post-amble, grab the contents of the port as soon as possible. Here's the code:
ISR(PORTC_VECT, ISR_NAKED) {
  uint8_t current;
  uint8_t ledon, ledoff;

  ledon=0b00100000; ledoff=0b0;

  asm volatile("\t"
  "push %0" "\t\n\t"
  "in %0,%1" "\t\n\t"
  : "=&r" (current)
  : "I" (_SFR_IO_ADDR(PINC))
  );
  PORTB=ledoff; // LOW

  // in r0, __SREG instruction saves SREG... then it's pushed onto the stack.
  asm volatile(
  "push r1" "\n\t"
  "push r0" "\n\t"
  "in r0, __SREG__" "\n\t" // 0x3f
  "push r0" "\n\t"
  "eor r1, r1" "\n\t"
  "push r18" "\n\t"
  "push r19" "\n\t"
  "push r20" "\n\t"
  "push r22" "\n\t"

By saving our current PORT state into the variable “current” at the very start of the ISR, using assembly language, we are able to get it as quickly as practicable. Note, however, that because of an ISR's special nature we can not be sure if the main code was using the register that will be used for “current” in the “%0” placeholder in the code: “in %0,%1”, above. Therefore, we must push it first... and take care to pop it last at the end of the ISR.
  "push %0" "\t\n\t"
  "in %0,%1" "\t\n\t"

Now that we have captured our PORT state as soon as possible, we ask: How well did we do? The screen says it took 992 ns... that's about 300 ns slower than a naked ISR preamble, or about 5 cycles. That's close to what we would expect from the assembly code: 2 cycles for the push, 1 for the in, and 1 for the out (to make the LED line go LOW). 4 instructions, or an expected 248ns slower than the routine with the PORTB=ledoff; command first.
...But we're still 62 ns off. What gives? According to my tests, over the course of many runs, there could be some significantly longer periods that the one just shown. Take this run for example:

This sort of thing happened infrequently, but over the course of a few runs one could find an outlier like this. My feeling is that sometimes the CPU may be in, for example, a timer interrupt and it is unable to service this interrupt until it's done. That's something to keep in mind.
Ultimately, the Pin Change Interrupts are a bit of an oddity. A single interrupt is called for any pin on a port that is triggered, and one needs software if one wants to determine which pin activated. Even then, there's no guarantee that the pin is in the same state that it was when the interrupt was triggered! Caveat programmer- you must be aware of of the capabilities of the hardware that you're working with, and of your system's own performance needs.
That said, I have used a relatively slow Pin Change Interrupt library with great success (http://code.google.com/p/arduino-pinchangeint/). Most cheap switches, for example, are quite bouncy so it's necessary to account for a certain degree of slop in the real world. This is what engineers are paid to do: Make components and systems work in the real world.
And that, my friends, is what they call Rocket Science: It ain't easy.
A Real Life Example of a Bouncy Switch
How well is the ISR grabbing the proper pin state on a fast-changing signal? “Fast” is relative, but for an Arduino running at 16 MHz I would say that fast is anything in the microsecond range. The Arduino's clock runs at a period of 62.5ns which is one machine instruction. In the space of 1 microsecond 16 (1-cycle) machine instructions can run... that's not a whole lot. Here is a real oscilloscope trace of a bouncy switch and of the Interrupt library reacting:

In this trace, the actions taken by the interrupt library are labelled A through G, in order to easily follow the sequence of events.

The interrupt library does the following:
ISR(PORTC_VECT, ISR_NAKED) {
  uint8_t current;
  uint8_t i;
  uint8_t interruptMask;
  uint8_t ledon, ledoff;

  ledon=0b00100000; ledoff=0b0;

  asm volatile("\t"
  "push %0" "\t\n\t"
  "in %0,%1" "\t\n\t"
  : "=&r" (current)
  : "I" (_SFR_IO_ADDR(PINC))
  );
  PORTB=ledoff; // LOW
  PORTB=ledon; // HIGH

Then:
    if (interruptMask & 0x01) {
  PORTB=ledoff; // LOW
  PORTB=ledon; // HIGH
  PORTB=ledoff; // LOW
  PORTB=ledon; // HIGH

The idea is this:
1. As soon as we've saved the current PORT state, send out a single pulse.
2. As soon as we've found the pin that on the port that we believe triggered the interrupt, send out a double pulse.
Now we can see when the interrupt triggers and when it thinks the pin state has changed. How does this line up against our bouncy switch? Are we properly reacting to all the activations?
Note, again, that this trace shows that the real world is a dirty dirty place. Inside the processor we can be very deterministic, but we have to be aware of what we are dealing with in order to design our systems properly. Here you can see the the bounces are coming microseconds apart; the X-axis time divisions are 10 microseconds. There are some significant pulses that appear less than 10 microseconds apart.
So let's evaluate the actions of the switch and the interrupt library, using the letter-labelled diagram as our guide...
# Pulses A and B

Zooming in on the two pulses, we see the library behave as expected: The switch (yellow trace) triggers the interrupt (blue trace) which reacts about 1us later. Then, about 5us later, we have determined which pin activated so if you look closely you can see that we send a double-pulse (if you can't see it, you'll just have to trust me). Oll Korrect.
At this point, we have saved the current state of the pins into a portSnapshot variable: When the interrupt activates next, we'll need to know which pin changed from this activation of the interrupt.
The pin's state will be saved at a LOW level
# Pulse C
This is interesting; Pulse C is on the left at the bottom zoomed-in view:

The interrupt is activated by the rising waveform on the left (note that the ATmega328's circuitry actually activated the interrupt somewhere prior to the rapid fall at the end of this sawtooth). This would be a change in the pin's state, however, by the time the interrupt reacts, the pin is at a low level (refer to the leftmost pulse in the blue trace at the bottom of the above screenshot). In variable “current”, then, the pin's state is LOW. “current” and the portSnapshot variable would thus look the same, the ISR believes that no pin has activated, and there is no activation of the user's function.
About 10 microseconds to the right of Pulse C, we find:
# Pulse D and E
Pulse D is the leftmost pulse on the bottom trace in the screenshot. Here again we see an activation on a rising pulse, but this rise is appreciably longer than Pulse C. Somewhere during the rise, the ATmega328 recognizes the rising signal, the interrupt triggers, and we capture the state of the port. This is important: because the ISR has time to recognize the HIGH level (note that the single pulse occurs while the sawtooth wave is still high, so “current” stores this level), there will be a change in the pin from what's saved in the “portSnapshot”. Again if you look closely you can see the double-pulse about 5 microseconds after the initial pulse.
The pin change is recognized and the portSnapshot stores HIGH level.
# Pulse F and G
Here we have an interrupt seemingly out of nowhere; about 5 microseconds after Pulse E comes Pulse F, a single pulse signifying entry of the ISR again. But there is no signal (yellow trace) to activate this ISR! ...Or isn't there?
Remember that the ISR at Pulse D acted on a HIGH transition. However, very soon after the ISR's first pulse we saw the signal transition rapidly to low. The ATmega328 recognized this transition, and tripped the PCIFx register (specifically, here, it's PCIF1)... it sets a flag to let the system know there is a pending interrupt. We couldn't act on the interrupt until the previous interrupt exited. However, once it did, we enter the ISR again. This was about 5 microseconds in total after executing the user's function in the previous ISR (which happens to be this:
volatile uint16_t interruptCount=0;
void interruptFunction() {
  interruptCount++;
}

). All the register pop's at the end of the ISR, the return to the main program, executing a single instruction in the main program (this is guaranteed by the system), and the return to the ISR took 5 microseconds. Note that because we have a high-level interrupt and there are no other interrupts set in this very simple system, we don't have to be concerned about another interrupt having used any of those 5 microseconds; this interrupt is PCINT1 and it's one of the highest interrupts on the system (see page 58 of the ATmega48A/48PA/88A/88PA/168A/168PA/328/328 datasheet).
So, to recap: During the ISR that acted on Pulse D, we flagged another interrupt due to the transition from HIGH to LOW. “portSnapshot” would have had registered HIGH for this pin, and now in the ISR for Pulse E “current” registers LOW for this pin. Thus, we find the changed pin and execute the users' interrupt routine at Pulse G.
# Implications
At the start of the Arduino sketch, prior to any switch activations, “current” shows a high value for our pin. We have seen at Pulse C that it's possible for us to miss a transition. Is it possible for us to miss a switch activation?
In the current circuit, we have essentially an RC circuit to V+ but a direct connection to ground. This would explain the sawtooth nature of the waveforms in the switch bounces:
Because of the longer rise time of the signal when the switch is open, when the initial trigger takes place the “current” variable is likely to report LOW. So we should see the transition, and record it properly.
However there is no guarantee, and we have not even taken into consideration other interrupts that may be set. If a fast-changing signal on a pin registers a transition (on any Pin Change Interrupt pin) while an ISR is being executed, there is a very good possibility that that pin's state will be misread. This makes Pin Change Interrupts a poor choice for fast-acting signals, and possibly even problematic in systems with a number of bouncy switches.
Again, however, multiple cheap bouncy rotary encoders have been used satisfactorily by the author with Pin Change Interrupts on the Arduino with an ATmega328p chip. The situation is not dire by any means, but again as always, Caveat Engineer; you must understand a system- that is, the Pin Change Interrupts- that is built on compromise and design accordingly.
# EnableInterrupt and PinChangeInt Comparison
## Sketch
void loop() {
  uint8_t led_on, led_off; // DEBUG
  led_on=0b00100000; led_off=0b0;

  //*led_port|=led_mask; // LED high
  PORTB=led_on;
  PORTC=0x01;
  Serial.println("---------------------------------------");
  delay(2000); // Every second,
  PORTC=0x00; // software interrupt, port A0
  PORTB=led_on;
  PORTB=led_off;
  PORTB=led_on;
  PORTB=led_off;
  PORTB=led_on;
## EnableInterrupt

## PinChangeInt